Fig. 1: Schematic depiction of one LED cube
Table 1: Used settings to process 3mm thick RMMA on a 40W laser cutter
The hippest Game in town
Polly
what
...
?

# Overview

# LED-Cubes
The game consists of 33 custom-cut acrylic glass (PMMA[1], Plexiglas®, perspex®, Lucite®) cubes of which 32 were 4cm in edge length and one 8x8x4cm in size to be the centre cube. The particular side walls were cut on a 40W laser cutter and glued together with superglue (UHU).
[1] Polymethyl methacrylate: Only use this material to cut, you get it the cheapest at the DIY store. When you go there, be sure to know the exact description and alternative descriptions. Don't trust anyone at the store to point you in the right direction or to sell you the right product.
To use the cubes as a 2D LED matrix, we wanted the system to be as flexible as possible and the cubes to be easily exchangeable. We thought of how to simply connect the cubes and came up with a connector consisting of two push pins (9mm in diameter) soldered to each side of a copper wire that leads from one side of a cube to the other. The pins were pre-processed (hit with a hammer) to make their heads flat.
Before cutting there was an immersion engraved into the outside centre of each sidewall (diameter: 11mm) so that the pin heads would fit evenly with the rest of the surface. Additionally an aperture 2,5mm in diameter was cut out in the centre of the immersion. To get the best results, we used the values in Table 1.
The pins were soldered onto the wire already put through both opposing apertures. The wire was then swirled in such way that it pulls both evenly towards the surface. Then an LED was soldered to the appropriate wires and hot glue was applied for stability and isolation purposes (see ).

# The frame

# Arduino Code